## Slide 1
JAMach14
Vehicle lifts activity
Progress report
Stakeholder session
27 September 2017
Ian FRASER
Project Coordinator

## Slide 2
Objectives of the activity
Check the conformity and safety of vehicle lifts against key requirements of the Machinery Directive
Ensure that non-compliant and unsafe vehicle lifts are brought into conformity or removed from the market
Examine the working of the conformity assessment procedures
Improve the general level of compliance
Discourage unfair competition

## Slide 3
Further objectives
Share experience of common market surveillance action and develop best practices – cooperation with Machinery ADCO
Develop cooperation with economic operators and their trade associations
Share ressources (technical experts)
Improve harmonised standards
Draw lessons for future market surveillance of machinery and similar products

## Slide 4
Scope of the activity
Participating authorities of 9 EU Member States:
BE, DK, FR, IE, LV, LU, MT, SE, UK
2 categories of vehicle lifts were targeted:
two-column lifts and scissor lifts
47 models of vehicle lift were inspected:
25 two-column vehicle lifts
22 scissor vehicle lifts

## Slide 5
Content of inspections
Checks on marking, DoC and instructions were carried out by the participating authorities
The inspection programme was based on selected specifications of the harmonised standard EN 1493
The main programme was limited by the need to avoid potentially destructive tests
Consequently, the inspections detect important non-conformities but do not establish full conformity of vehicle lifts
Notes: 5

## Slide 6
Main method for inspection
Vehicle lifts were inspected at the premises of the owner (importer, distributor, user)
Inspection was carried out by local inspectors assisted by a JAMach14 technical expert, who then drew up an inspection report
2 technical experts:
  Christer Danielsson (Sweden)
  Jacques Ducasse (France)

## Slide 7
Other inspection methods
In view of the limitations of the main method, other methods were also used:
In DK, 4 vehicle lifts were taken for inspection and testing then returned to the economic operators
6 vehicle lifts were purchased ( FR, UK) and installed in the premises of the authorities for more thorough testing and inspection

## Slide 8
‘Administrative’ issues
There were many ‘administrative’ failings,
for example:
Name plate:
    No identification of manufacturer (8/47)
    No country of manufacture (11/47)
    No designation of the machinery (14/47)
Declaration of conformity:
    No Declaration of conformity (11/47)
    No identification of machinery (5/47)
    Incorrect references of Directives or of harmonised standards (5/47)
Notes: 8

## Slide 9
Instructions for use
There were many omissions relating to the instructions for use, for example:
    No instructions for the vehicle lift (3/47)
    Instructions not translated (6/47)
    No instructions for inspection, trouble-shooting or replacement of parts (10/47)
    No instructions for checks before putting into service (9/47)
    No warning not to climb on to the load (14/47)
Notes: 9

## Slide 10
Most frequent technical
non-conformities (EN 1493)
5.17 - Lack of protection against pinching and shearing (18/47)
5.21 - Non-compliant electrical equipment (13/47)
5.12 - Risk due to unintended blockage of load carrying device (13/47)
5.14.2 - Inadequate protection against leakage (11/47)
5.8.1, 5.8.2 - Lack of means to prevent inadvertent motion (11/47)
6.1.5 - Failure in practical tests (9)
Notes: 10

## Slide 11
Other frequent
non-conformities
5.9.5 - Inadequate locking systems of load-carrying arms (11/47)
5.8.3.1 - Lack of derailment protection (9/47)
5.7.4 – Load distribution not reversible (8/47)
5.3.5 - Lack of means to prevent inadvertent operation (7/47)
5.3.4 - Lack of marking on control devices (7/47)
5.15 - Lack of synchronisation between load carrying devices (5/47)
5.8.3.2 - Lack of safety at nip points (5/47)
Notes: 11

## Slide 12
Risk assessment
The authorities assess the risks associated with the non-conformities detected, using the RAPEX risk assessment method
Examples:
    A vehicle falls on the operator following the failure of an inadequate carrying arm locking system
    = SERIOUS RISK
    Due to lack of protection, the operator’s foot is crushed under the lifting arm
    = MEDIUM RISK
Notes: 12

## Slide 13
Follow-up actions
In light of the risk assessment, each authority contacts the economic operators concerned to ensure that appropriate measures are taken with respect to the non-compliant and unsafe vehicle lifts it has inspected
Possible actions:
    Bringing into conformity
    Withdrawal from the market
    Recall from users
Wherever possible, the measures are voluntary
Where necessary, the measures are mandatory
Notes: 13

## Slide 14
Follow-up in the EEA
In case of serious risk, the product is notified to the Commission and to the other market surveillance authorities via RAPEX (system for Rapid Exchange of information)
The objective is to ensure that the necessary corrective measures are taken throughout the EEA
The other cases will be reported to all EEA market surveillance authorities for Machinery via the market surveillance database ICSMS and to the Machinery ADCO Group
Notes: 14