## Slide 1: STUDY 2015 ON VEHICLE EMISSIONS IN PERIODIC TECHNICAL INSPECTIONS (LIGHT VEHICLES - HEAVY VEHICLES)
SCHEDULING
Shipment of equipment to UTAC : until july the 31th
Warm-up meeting in UTAC with manufacturer : August 27th
Launch of the test period : september the 3rd
Analysis of results and return : end of 2015

## Slide 2: STUDY 2015 ON VEHICLE EMISSIONS
HISTORICAL
2012 and 2013 : priority action program of study on road vehicles in service and national implementation measures directly or indirectly related to the improvement of environmental protection, led by UTAC_OTC
Analysis of technical controls available
New test equipment are still in development or discussed

## Slide 3: STUDY 2015 ON VEHICLE EMISSIONS
NOWADAYS
OPACIMETER
  Evolution in order to pass under the threshold of 0,5m-1
  Taken into account and uses of the value of UNECE R24 (severe)
  Test procedure updated  removal of particle filter detection
  Other axis :
  By LASER  mass equivalent of particle , for a lower threshold
  By NOx concentration  using engine idle, for EGR operating fault
  By OBD scanning  as a complementary solution (for EURO 6)
Proposal for opacimeter focused on :
  detecting particles,
  the status of the EGR valve by measuring Nox

## Slide 4: STUDY 2015 ON VEHICLE EMISSIONS
AIM
Do devices on the market can be used in technical control ?
Allowing a decision on the compliance on recent vehicle generations concerned by emissions of particulate
Identifying malfunctions of the EGR valve
MEANS
Comparison by laboratory tests performed on the vehicle homologation basis
UTAC :
  test vehicle bench 4x2
  particle counter of the test vehicle bench
  Opacimeter AVL 439 (UNECE R24 compliant)
  Gas analyzer of the test vehicle bench
  EOBD tool
  Vehicles : direct and indirect injection for petrol engine, diesel EURO 5 and EURO 6 (SCR)
Equipment manufacturer:
  particulate analyzer system (3 suppliers)
  NOx analyzer system (1 supplier)
  Gas analyzer for petrol engine used in periodic technical inspections

## Slide 5: STUDY 2015 ON VEHICLE EMISSIONS
Test procedures
Phase 1 :
homologation cycle for emission on vehicle : using test bench system and manufacturer device
Phase 2 :
vehicle deterioration (Particle Filter, EGR valve, SCR)
Report
Evaluation of the tests results,
Extending of study (unoffical)
For new advancement, need of adjustment and investigation an add on proposal can be available for any equipment manufacturer.