Working Group 6 of the European Garage Equipment Association, held on:

Tuesday 23rd June 2009, 10h00 – 17h00

EGEA offices

42 boulevard de Weluwe

Brussels

Opening and welcome – Mr. Olivier Sauzay, WG6 Chairman.

1. Participants.

Stefan VELKOSKI

Frank BEAUJEAN

Emanuele LUSUARDI

Olivier SAUZAY

Jaume BERENGUER

Jordi BRUNET

Dave GARRAT, GianFranco CROSTA and Carlos Diez IZARRA are excused.

2. Topics for discussion

New Directive 2009/40 replacing 96/96

Political part is modified. Annexe II will be probably modified before the end of the year (proposal in June and decision in November), and annexe I may be within two years

Analysis of the reports of each association about the national brake tester homologation specification.

No discussion

Draft of the Italian specification proposal for HGV RBT.

On the French point of view, there is a great correspondence between French specifications and Italian proposal except the motor approval and the mandatory need of pressure or pedal measurement.

On the German point of view, many differences with the German regulations make an economical problem if this text should be applied in Germany (motor brakes mandatory, motor approval, only one type of maximum weight, ...)

On Spanish point of view, the specification is convenient.

Comments on the EGEA Preliminary comments on revision of Directive 96/96

Point 1.2.2      Efficiency

Participants agree with the proposal

Point 2.4    Check alignment

Commission proposal requires vehicle manufacturer’s data but there is no data for side slip test. So solution 2 cannot be used without modification of the defect definition.

Point 5.3.2    Suspension system

At the moment EGEA WG6 works on the accuracy and correlation of imbalance measurement with all the existing benches.

Emanuele LUSUARDI takes contact with the Italian participant to the European commission about 96/96 in order to understand the way of managing the evolution of this document.

Suspension measurement studies.

The goal is to make comparison tests between the results provided by different suspension benches and the Speed/effort diagram used by car and shock absorbers manufacturers, in order to evaluate the possibility to build a correlation between these results.

Comparison between the benches will be made :

- on the accuracy of imbalance in order to improve the existing PTI tests

- on the correlation with the shock absorber manufacturer reference.

4 benches/principles will participate to the tests :

MAHA / SNAP ON (1),

BEISSBARTH (2),

ACTIA MULLER (3),

VTEQ (4).

There are no fitting problem. Benches can be installed everywhere

(1) and (4) need ramps with hieght 280mm

(3) can have ramps 280 mm or nothing

(2) has no need

Selection of the cars will be made by Monroe in regards of the available worn shock absorbers

The aim is to check 5 cars of different types with normal tire pressure and normal weight but by changing the Speed/force value of the shock absorbers with 20%, 50% and 100% of efficiency.

If time is enough tests will also be made on tire pressure effect.

Olivier SAUZAY keeps contact with Tenneco / Monroe in order to organise the test session at the end of September or in October.

Next meeting.

Next meeting is proposed in GIEG offices the 12 October, 10.00 am, if the suspension test meeting has not been already scheduled.

To be confirmed.